## Slide 1: Exercise 16a Forced Landings
Aim - as syllabus
Phase 6
Copyright Marcus Furniss 2025

## Slide 2: Why Would an Engine Fail?
Whilst unlikely, there are many potential causes for a power loss or engine failure;
Fuel Delivery
  Blockages, pump failure, fuel contamination or simply running out
Electrical
  We check the electrical system is working correctly before flight
Lubrication
  Always check we have sufficient oil before flight
Mechanical Failure
  Full or partial engine failure…

## Slide 3: Partial Engine Failures
Following a PEF adopt the optimum attitude/speed to sustain level flight or minimise height loss whilst maintaining a safe margin above the stall speed
C42 minimum 50KTS, EV97 minimum 60mph
Assess whether the aircraft can maintain level flight
If the aircraft cannot maintain level flight:
  Treat as a full engine failure
  Possibly utilise the remaining power to expand the choice of possible landing areas before commencing the forced landing procedure

## Slide 4: Partial Engine Failures
If the aircraft can maintain level flight:
  Transit to an area where better options for forced landings are available
  Be prepared for the engine to stop at any time
  Consider continuing to an even better option such as an airfield, remaining within gliding range of safe areas
  Make a radio call if appropriate
  If height and time permit appropriate checks
  If engine condition deteriorates further, be prepared…
  Land as soon as is practicable at the nearest and safest location
  Position the aircraft for a glide approach (which will avoid the danger associated with a further loss of power)

## Slide 5: Forced Landings 16a
Whilst unlikely, aircraft should always be operated with the possibility of an engine failure or partial engine failure
Consider potential landing options in relation to position and height
  Rember to use altimeter with caution
Avoid flight over large areas of un-landable terrain
Maintain required skills with regular practice
Failure to do so may result in…

## Slide 6
2000 AGL
1
Fly The Aircraft

## Slide 7: 1.Fly the Aircraft!
Adopt gliding attitude, attain min sink and trim
  In general with low energy aircraft like microlights, immediately lower nose to obtain gliding attitude to avoid loss of airspeed and possible stall
Min Sink C42 = 45 KTS, EV-97 = 60 MPH
  In high performance types like C42 and EV-97 if airspeed is significantly higher than min sink speed then it may be beneficial to raise nose and convert speed to height
Amendment to the above - Instructor will brief reasons for using best glide rather than min sink after full or partial engine failure

## Slide 8
2000 AGL
(min sink and trim)
1
Fly The Aircraft

## Slide 9
1900 AGL
1
(min sink and trim)
Fly The Aircraft
2
Estimate Wind

## Slide 10: 2.Estimate Wind Direction and Strength
We should always aim to land into wind
Smoke
Surface indications
  Wind patterns in standing crop
  Ripples on water – reflective, non-rippled areas are at upwind end
Drift
  Airspeed v Ground speed / Heading v Track
Known local wind
  Make a note when carrying out pre flight checks
Cloud shadow
  Allow for surface wind to back approx 30 degrees v wind at altitude

## Slide 11
1900 AGL
1
(min sink and trim)
Fly The Aircraft
2
Estimate Wind

## Slide 12
1900 AGL
1
Fly The Aircraft
2
Estimate Wind
Wind
(min sink and trim)

## Slide 13
1800 AGL
1
Fly The Aircraft
2
Estimate Wind
3
Select Landing Area
Wind
(min sink and trim)

## Slide 14: 3.Select Landing Area
Gliding range
  Select a landing area close enough to glide to and with enough height to fly safe procedure
  Range will depend on wind
  Initially look left and low, then all around (C42/Ev-97)
  If no suitable areas can be seen, turn downwind
Size
  Big is better but should be at least long enough to allow for minor errors of judgement, sink, lift etc
Shape
  Shape should allow sufficient length to land into wind
  Check that intended landing area is clear of power cables and fences
  Remember posts are easier to spot than the wires themselves

## Slide 15: 3.Select Landing Area
Surface
  As smooth and firm as possible, ideally short grass or cut crop
  If tractor lines, try to land in their direction
  Ploughed fields or standing crop not ideal
  ‘Green is good, brown is bad, light brown…could be OK’
Shoots
  Over and undershoots – ideally pick a landing area that allows for errors in judgement or unexpected sink – if your initial procedure is not going to plan then consider an alternative field
Civilization
  If landing options are all poor and there is a high chance of damage, than consider those closer to habitation/roads as this will enable you to more easily get outside assistance should it be required

## Slide 16
1800 AGL
1
Fly The Aircraft
2
Estimate Wind
3
Select Landing Area
Wind
(min sink and trim)

## Slide 17
1700 AGL
1
Fly The Aircraft
2
Estimate Wind
3
Select Landing Area
4
Fly the Plan
Wind
(min sink and trim)

## Slide 18
1
Fly The Aircraft
2
Estimate Wind
3
Select Landing Area
4
Fly the Plan
Wind
Approx 1000’ AGL
Constant angle
Constant Aspect Method
High Key Point
(min sink and trim)
1700 AGL
Approx 500’ AGL
Best Glide
Flaps as required
Approx 300’ AGL
Low Key Point
Wings level
Flaps as required
INITIAL AIM 1/2
FINAL AIM 1/3

## Slide 19
1
Fly The Aircraft
2
Estimate Wind
3
Select Landing Area
4
Fly the Plan
Wind
Approx 1000’ AGL
Constant angle
Constant Aspect Method
High Key Point
(min sink and trim)
1700 AGL
Best Glide
Flaps as required
Approx 300’ AGL
Low Key Point
Wings level
Flaps as required
INITIAL AIM 1/2
FINAL AIM 1/3
IF TOO LOW
IF TOO HIGH
Sideslip / S-turns
Approx 500’ AGL

## Slide 20
1
Fly The Aircraft
2
Estimate Wind
3
Select Landing Area
4
Fly the Plan
Wind
Approx 1000’ AGL
Constant angle
Constant Aspect Method
High Key Point
(min sink and trim)
1700 AGL
Best Glide
Flaps as required
Approx 300’ AGL
Low Key Point
Wings level
Flaps as required
INITIAL AIM 1/2
FINAL AIM 1/3
IF TOO LOW
IF TOO HIGH
Sideslip / S-turns
Approx 500’ AGL

## Slide 21
1
Fly The Aircraft
2
Estimate Wind
3
Select Landing Area
4
Fly the Plan
Wind
Approx 1000’ AGL
Constant angle
Constant Aspect Method
High Key Point
(min sink and trim)
1600 AGL
Approx 500’ AGL
Best Glide
Flaps as required
Approx 300’ AGL
Low Key Point
Wings level
Flaps as required
INITIAL AIM 1/2
FINAL AIM 1/3
IF TOO LOW
IF TOO HIGH
Sideslip / S-turns
Mayday Call
5

## Slide 22: Once you are flying the plan;
5. Mayday Call
  Frequency in use or 121.5, transponder to 7700…but only if this doesn’t distract from the flying

## Slide 23
1
Fly The Aircraft
2
Estimate Wind
3
Select Landing Area
4
Fly the Plan
Wind
Approx 1000’ AGL
Constant angle
Constant Aspect Method
High Key Point
(min sink and trim)
1600 AGL
Best Glide
Flaps as required
Approx 300’ AGL
Low Key Point
Wings level
Flaps as required
INITIAL AIM 1/2
FINAL AIM 1/3
IF TOO LOW
IF TOO HIGH
Sideslip / S-turns
Mayday Call
5
Approx 500’ AGL

## Slide 24
1
Fly The Aircraft
2
Estimate Wind
3
Select Landing Area
4
Fly the Plan
Wind
Approx 1000’ AGL
Constant angle
Constant Aspect Method
High Key Point
(min sink and trim)
1500 AGL
Best Glide
Flaps as required
Approx 300’ AGL
Low Key Point
Wings level
Flaps as required
INITIAL AIM 1/2
FINAL AIM 1/3
IF TOO LOW
IF TOO HIGH
Sideslip / S-turns
Mayday Call
5
Attempt Restart
6
Approx 500’ AGL

## Slide 25: Once you are flying the plan;
5. Mayday Call
  Frequency in use or 121.5, transponder to 7700…but only if this doesn’t distract from the flying
6. Attempted restart
  Check ignition on, fuel on, Carb heat if appropriate

## Slide 26
1
Fly The Aircraft
2
Estimate Wind
3
Select Landing Area
4
Fly the Plan
Wind
Approx 1000’ AGL
Constant angle
Constant Aspect Method
High Key Point
(min sink and trim)
1500 AGL
Best Glide
Flaps as required
Approx 300’ AGL
Low Key Point
Wings level
Flaps as required
INITIAL AIM 1/2
FINAL AIM 1/3
IF TOO LOW
IF TOO HIGH
Sideslip / S-turns
Mayday Call
5
Attempt Restart
6
Approx 500’ AGL

## Slide 27
1
Fly The Aircraft
2
Estimate Wind
3
Select Landing Area
4
Fly the Plan
Wind
Approx 1000’ AGL
Constant angle
Constant Aspect Method
High Key Point
(min sink and trim)
1400 AGL
Best Glide
Flaps as required
Approx 300’ AGL
Low Key Point
Wings level
Flaps as required
INITIAL AIM 1/2
FINAL AIM 1/3
IF TOO LOW
IF TOO HIGH
Sideslip / S-turns
Mayday Call
5
Attempt Restart
6
T.I.F.S Check
7
Approx 500’ AGL

## Slide 28: Once you are flying the plan;
5. Mayday Call
  Frequency in use or 121.5, transponder to 7700…but only if this doesn’t distract from the flying
6. Attempted restart
  Check ignition on, fuel on, carb heat if appropriate
7. T.I.F.S check
  Throttle closed
  Ignition off, Master off when RT complete
  Fuel off
  Security – check harness tight, reassure passenger

## Slide 29
1
Fly The Aircraft
2
Estimate Wind
3
Select Landing Area
4
Fly the Plan
Wind
Approx 1000’ AGL
Constant angle
Constant Aspect Method
High Key Point
(min sink and trim)
1400 AGL
Best Glide
Flaps as required
Approx 300’ AGL
Low Key Point
Wings level
Flaps as required
INITIAL AIM 1/2
FINAL AIM 1/3
IF TOO LOW
IF TOO HIGH
Sideslip / S-turns
Mayday Call
5
Attempt Restart
6
T.I.F.S Check
7
Approx 500’ AGL

## Slide 30
1
Fly The Aircraft
2
Estimate Wind
3
Select Landing Area
4
Fly the Plan
Wind
Approx 1000’ AGL
Constant angle
Constant Aspect Method
High Key Point
(min sink and trim)
Best Glide
Flaps as required
Approx 300’ AGL
Low Key Point
Wings level
Flaps as required
INITIAL AIM 1/2
FINAL AIM 1/3
IF TOO LOW
IF TOO HIGH
Sideslip / S-turns
Mayday Call
5
Attempt Restart
6
T.I.F.S Check
7
Approx 500’ AGL

## Slide 31
Keep in balance during turns and monitor safe A/S
Try to limit turns to 30 deg bank angle
Flaps as appropriate
1200 AGL
Beats and Turns Method
If too low for circuit method
INITIAL AIM 1/2
Full Flaps /Sideslip
Wings level
FINAL AIM 1/3
Wind
Best Glide
1st Stage flaps
Position aircraft on Beat line/Base leg
1
Fly The Aircraft
2
3
Asses Wind
Select Landing Area
Fly the Plan
4
REFERENCE LINE OR POINT
To prevent aircraft migration towards field
Mayday Call
5
Attempt Restart
6
T.I.F.S Check
7

## Slide 32: Landing
Touchdown
  Surface unknown, so land as softly as possible and fully held off to minimise touchdown speed
  If landing on crop treat top of crop as landing surface
After landing
  Secure aircraft – check position and livestock
  Cancel mayday – by radio or phone
  Notify destination within 30 mins of your planned arrival time
  Notify land owner
  Consider very carefully take off and only if absolutely sure cause identified and rectified

## Slide 33: Airmanship for Practice Engine Failure
Lookout
Be mindful of the 500’ rule
Choose multiple sites to practice – don’t be a nuisance
Consider the descent and climb out path
  Always be ready for real engine failure
  Ensure decent and climb out are free from obstructions
Warm engine in the descent
  Helps prevent carburettor icing
  When going around increase power gradually and raise nose, then retract flaps in stages
Manage airspeed in go around – respect Vfe

## Slide 34: Exercise 16a Forced Landings
Questions?