## Slide 1: Exercise 12 Circuit Training
Aim - as syllabus
Phase 4
Copyright Marcus Furniss 2019

## Slide 2: 2015 – Amendment to following presentation;
Due to movement in magnetic variation
Runway 27 is now 26
Runway 09 is now 08

## Slide 3: The Circuit
What is the purpose of The Circuit?

## Slide 4: The Circuit
The circuit is a standard path for coordinating air traffic around an airfield, as safely as possible
By using a consistent flight pattern pilots will know from where to expect other air traffic, and be able to see it and avoid it

## Slide 5: The Circuit
Over several sessions we will learn
  Circuit procedures
  To fly the circuit accurately and safely
  Different take off and landing techniques
  To deal with circuit emergencies
Plenty of practice is required to build up skills!

## Slide 6: The Standard Into Wind Take Off
Before Take Off
  Pre take off checks - VITAL ACTIONS
  Flap setting for conditions and surface
  Look out before entering runway
  If ATC obtain permission before entering runway
  On lining up check correct runway using compass

## Slide 7: The Runways at Barton
6 runway directions
  26/08
  02/20
  32/14
We land and take off into wind to
  Reduce take off ground speed and distance
  Reduce landing ground speed and distance

## Slide 8: The 26 Circuit at Barton
Final
Wind from the West (260)
LIVE SIDE
DEAD SIDE
Climb Out
Downwind
Base
Crosswind
26
08

## Slide 9: The 26 Circuit at Barton
LOOK OUT
LOOK OUT
LOOK OUT
600’ turn onto Crosswind Leg
FAWTH checks
RT call
60 mph, 2nd / 3rd Flaps
RT call
Final
Climb Out
Accelerate to Vy - 70 mph
Above 300’ AGL retract flaps and adopt 80 mph
Downwind
Base
Crosswind
At 1000’ level out and trim - airspeed 90 mph
27
09
LOOK OUT
45 Deg
PAT descent
70 mph, Ist Flaps
Check parallel to runway
Check to Dead side for joining traffic

## Slide 10: The 26 Circuit at Barton
Wind from West

## Slide 11: The 08 Circuit at Barton
Wind from the East (080)
LIVE SIDE
DEAD SIDE
Final
Climb Out
Downwind
Base
Crosswind
26
08

## Slide 12: The 08 Circuit at Barton
LOOK OUT
45 Deg
LOOK OUT
LOOK OUT
600’ turn onto Crosswind Leg
LOOK OUT
Final
Climb Out
Downwind
Base
Crosswind
FAWTH checks
RT call
27
09
Accelerate to Vy - 70 mph
Above 300’ AGL retract flaps and adopt 80 mph
60 mph, 2nd / 3rd Flaps
RT call
PAT descent
70 mph, Ist Flaps
At 1000’ level out and trim - airspeed 90 mph
Check parallel to runway
Check to Dead side for joining traffic

## Slide 13: The 08 Circuit at Barton
Wind from East

## Slide 14: The Standard Into Wind Take Off
Take Off
  Line up on centreline
  Nose wheel straight
  Stick slightly aft of neutral
  Look ahead for reference point
  Release brakes (heels on floor EV-97)
  Smoothly apply full power over 3 seconds

## Slide 15: The Standard Into Wind Take Off
Take Off
  Use rudder as appropriate to keep straight
    Anticipate and correct yaw to left with right rudder
  Keep wings level with ailerons
  Confirm full power has been achieved and airspeed is rising
  Apply back pressure on stick to raise nose wheel just above the ground and hold this nose attitude until lift off

## Slide 16: The Standard Into Wind Take Off
Climb Out
  As aircraft lifts off prevent the nose from pitching up
  Adopt shallow climbing angle and accelerate to 70 mph
  Keep wings level with aileron, in balance with rudder
  Aim at reference point to track on centreline of runway

## Slide 17: Standard Into Wind Powered Approach
Advantages
  Uses power to accurately control the descent path
  Reduces effects of turbulence and wind gradient
  Less steep – more comfortable for passengers
Approach path controlled by coordinated use of
Power to control descent path (Height)
Elevator (Pitch) to control Airspeed

## Slide 18: Standard Into Wind Powered Approach
Circuit planning
  Constantly keep a vigilant look out
  Avoided conflict with other circuit traffic by adjusting airspeed or widen/lengthen circuit as appropriate
  Flatter descent for powered approach compared to glide approach
On Base Leg initiate descent
  Allow for drift
  PAT to achieve 70 mph and 1st Flaps (ensure airspeed below Vfe)
  Adjust power (medium low) to establish correct approach angle

## Slide 19: Standard Into Wind Powered Approach
Turn onto Final
  Look long and low before turning
  Judge the turn so you line up on the extended runway centreline
Establish Final approach
  Correct airspeed (60 mph EV-97)
  Landing flaps set
  Medium low power setting
Pick an aiming point
  Aim at reference point on the runway (just after the runway numbers)
Reference Point

## Slide 20: Standard Into Wind Powered Approach
The reference point should stay stationary in your view
If reference point is rising in your field of view then you are sinking below the approach path
  Increase power and raise the nose a little
Planned approach path

## Slide 21: Standard Into Wind Powered Approach
If reference is descending in your field of view then you are rising above the approach path
  Reduce power and lower the nose a little
Planned approach path

## Slide 22: Round Out
Maintain the correct airspeed (60mph EV-97, 55KT C42)
At approximately 30 feet above the ground
  Transfer your gaze from the aiming point to the far end of the runway
  Easy back on the stick to end up in a level attitude approximately 3 feet (1 metre) above the ground
approach

## Slide 23: Hold Off
Reduce the power to idle
  (This may have been done earlier to maintain correct approach path)
As airspeed reduces ease back on the stick to raise the nose to balance any tendency to sink
  (This increases AOA which counters the loss in lift due reducing airspeed)
Maintaining hold off height accurately involves developing both skill and judgement through practice
Maintain runway centreline using small aileron inputs to counter any drift

## Slide 24: Hold Off - Common Issues
Height judgement – refine skills, remember to look ahead
Not holding off long enough
  Landing too fast, difficult to control, possibly nose wheel first
  Patient required – wait for nose attitude to be correct for touch down
Ballooning at round out
  Too much backward pressure on stick
  If airspeed sufficient, check pressure on stick and wait for aircraft to settle to correct height and continue with hold off
Ballooning in hold off
  Too high and slow airspeed – GO AROUND

## Slide 25: Touch down
Continue to hold off, allowing aircraft to lower towards ground - HAVE PATIENCE
Ensure aircraft is tracking down runway
  Use rudder to align fuselage
  Ailerons to control lateral drift
Aim to touchdown with airspeed at a minimum
  Stick being nearly fully back
  Nose high attitude (the Flare)
  Nose wheel clear of the runway

## Slide 26: Roll Out
Once on ground:
  steer with rudder
  maintain back pressure on stick until nose wheel lowers
Brake gently if necessary
Once at safe taxi speed vacate runway
  Post landing checks
  ATC clearance to taxi

## Slide 27: Additional Comments
Basic principles of the circuit applies to all airfields
  Standard circuits are LH unless informed otherwise
  Circuit heights at other airfields may vary between 500’ and 1000’
  Remember that the QFE pressure setting is used in the circuit