## Slide 1: Exercise 16a Forced Landings
Aim - as syllabus
Phase 6
Copyright Marcus Furniss 2019

## Slide 2: Why Would an Engine Fail?
Whilst unlikely, there are many potential causes for a power loss or engine failure;
Fuel Delivery
  Blockages, pump failure, fuel contamination or simply running out
Electrical
  We check the electrical system is working correctly before flight
Lubrication
  Always check we have sufficient oil before flight
Mechanical Failure
  Treat a rough running engine as an engine failure

## Slide 3: Forced Landings 16a
Whilst unlikely, aircraft should always be operated with the possibility of an engine failure
Consider potential landing options in relation to position and height
Avoid flight over large areas of unlandable terrain
Maintain required skills with regular practice
Failure to do so may result in…

## Slide 4
2000 AGL
1
Fly The Aircraft

## Slide 5: Fly the Aircraft!
Adopt gliding attitude attain min sink and trim
  In general with low energy aircraft like microlights, immediately lower nose to obtain gliding attitude to avoid loss of airspeed and possible stall
Min Sink C42 = 45 KTS, EV-97 = 60 MPH
  In high performance types like C42 and EV-97 if airspeed is significantly higher than min sink speed then it may be beneficial to raise nose and convert speed to height

## Slide 6
2000 AGL
(min sink and trim)
1
Fly The Aircraft

## Slide 7
1900 AGL
1
(min sink and trim)
Fly The Aircraft
2
Estimate Wind

## Slide 8: Estimate Wind Direction and Strength
We should always aim to land into wind
Smoke
Surface indications
  Wind patterns in standing crop
  Ripples on water – reflective, non-rippled areas are at upwind end
Drift
  Airspeed v Ground speed / Heading v Track
Known local wind
  Make a note when carrying out pre flight checks
Cloud shadow
  Allow for surface wind to back approx 30 degrees v wind at altitude

## Slide 9
1900 AGL
1
(min sink and trim)
Fly The Aircraft
2
Estimate Wind

## Slide 10
1900 AGL
1
Fly The Aircraft
2
Estimate Wind
Wind
(min sink and trim)

## Slide 11
1800 AGL
1
Fly The Aircraft
2
Estimate Wind
3
Select Landing Area
Wind
(min sink and trim)

## Slide 12: Select Landing Area
Gliding range
  Select a landing area close enough to glide to and with enough height to fly safe procedure
  Range will depend on wind
  Initially look left and low, then all around (C42/Ev-97)
  If no suitable areas can be seen, turn downwind
Size
  Big is better but should be at least long enough to allow for minor errors of judgement, sink, lift etc
Shape
  Shape should allow sufficient length to land into wind
  Check that intended landing area is clear of power cables and fences
  Remember posts are easier to spot than the wires themselves

## Slide 13: Select Landing Area
Surface
  As smooth and firm as possible, ideally short grass or cut crop
  If tractor lines, try to land in their direction
  Ploughed fields or standing crop not ideal
  ‘Green is good, brown is bad, light brown…could be OK’
Shoots
  Over and undershoots – ideally pick a landing area that allows for errors in judgement or unexpected sink
Civilization
  If landing options are all poor and there is a high chance of damage, than consider those closer to habitation/roads as this will enable you to more easily get outside assistance should it be required

## Slide 14
1800 AGL
1
Fly The Aircraft
2
Estimate Wind
3
Select Landing Area
Wind
(min sink and trim)

## Slide 15
1700 AGL
1
Fly The Aircraft
2
Estimate Wind
3
Select Landing Area
4
Fly the Plan
Wind
(min sink and trim)

## Slide 16
1
Fly The Aircraft
2
Estimate Wind
3
Select Landing Area
4
Fly the Plan
Wind
Approx 1000’ AGL
Constant angle
Constant Aspect Method
High Key Point
(min sink and trim)
1700 AGL
Approx 500’ AGL
Best Glide
Flaps as required
Approx 300’ AGL
Low Key Point
Wings level
Flaps as required
INITIAL AIM 1/2
FINAL AIM 1/3

## Slide 17
1
Fly The Aircraft
2
Estimate Wind
3
Select Landing Area
4
Fly the Plan
Wind
Approx 1000’ AGL
Constant angle
Constant Aspect Method
High Key Point
(min sink and trim)
1700 AGL
Best Glide
Flaps as required
Approx 300’ AGL
Low Key Point
Wings level
Flaps as required
INITIAL AIM 1/2
FINAL AIM 1/3
IF TOO LOW
IF TOO HIGH
Sideslip / S-turns
Approx 500’ AGL

## Slide 18
1
Fly The Aircraft
2
Estimate Wind
3
Select Landing Area
4
Fly the Plan
Wind
Approx 1000’ AGL
Constant angle
Constant Aspect Method
High Key Point
(min sink and trim)
1700 AGL
Best Glide
Flaps as required
Approx 300’ AGL
Low Key Point
Wings level
Flaps as required
INITIAL AIM 1/2
FINAL AIM 1/3
IF TOO LOW
IF TOO HIGH
Sideslip / S-turns
Approx 500’ AGL

## Slide 19
1
Fly The Aircraft
2
Estimate Wind
3
Select Landing Area
4
Fly the Plan
Wind
Approx 1000’ AGL
Constant angle
Constant Aspect Method
High Key Point
(min sink and trim)
1600 AGL
Approx 500’ AGL
Best Glide
Flaps as required
Approx 300’ AGL
Low Key Point
Wings level
Flaps as required
INITIAL AIM 1/2
FINAL AIM 1/3
IF TOO LOW
IF TOO HIGH
Sideslip / S-turns
Mayday Call
5

## Slide 20: Fly The Plan
5. Mayday Call
  Frequency in use or 121.5, transponder to 7700…but only if this doesn’t distract from the flying

## Slide 21
1
Fly The Aircraft
2
Estimate Wind
3
Select Landing Area
4
Fly the Plan
Wind
Approx 1000’ AGL
Constant angle
Constant Aspect Method
High Key Point
(min sink and trim)
1600 AGL
Best Glide
Flaps as required
Approx 300’ AGL
Low Key Point
Wings level
Flaps as required
INITIAL AIM 1/2
FINAL AIM 1/3
IF TOO LOW
IF TOO HIGH
Sideslip / S-turns
Mayday Call
5
Approx 500’ AGL

## Slide 22
1
Fly The Aircraft
2
Estimate Wind
3
Select Landing Area
4
Fly the Plan
Wind
Approx 1000’ AGL
Constant angle
Constant Aspect Method
High Key Point
(min sink and trim)
1500 AGL
Best Glide
Flaps as required
Approx 300’ AGL
Low Key Point
Wings level
Flaps as required
INITIAL AIM 1/2
FINAL AIM 1/3
IF TOO LOW
IF TOO HIGH
Sideslip / S-turns
Mayday Call
5
Attempt Restart
6
Approx 500’ AGL

## Slide 23: Fly The Plan
5. Mayday Call
  Frequency in use or 121.5, transponder to 7700…but only if this doesn’t distract from the flying
6. Attempted restart
  Check ignition on, fuel on, Carb heat if appropriate

## Slide 24
1
Fly The Aircraft
2
Estimate Wind
3
Select Landing Area
4
Fly the Plan
Wind
Approx 1000’ AGL
Constant angle
Constant Aspect Method
High Key Point
(min sink and trim)
1500 AGL
Best Glide
Flaps as required
Approx 300’ AGL
Low Key Point
Wings level
Flaps as required
INITIAL AIM 1/2
FINAL AIM 1/3
IF TOO LOW
IF TOO HIGH
Sideslip / S-turns
Mayday Call
5
Attempt Restart
6
Approx 500’ AGL

## Slide 25
1
Fly The Aircraft
2
Estimate Wind
3
Select Landing Area
4
Fly the Plan
Wind
Approx 1000’ AGL
Constant angle
Constant Aspect Method
High Key Point
(min sink and trim)
1400 AGL
Best Glide
Flaps as required
Approx 300’ AGL
Low Key Point
Wings level
Flaps as required
INITIAL AIM 1/2
FINAL AIM 1/3
IF TOO LOW
IF TOO HIGH
Sideslip / S-turns
Mayday Call
5
Attempt Restart
6
T.I.F.S Check
7
Approx 500’ AGL

## Slide 26: Fly The Plan
5. Mayday Call
  Frequency in use or 121.5, transponder to 7700…but only if this doesn’t distract from the flying
6. Attempted restart
  Check ignition on, fuel on, carb heat if appropriate
7. T.I.F.S check
  Throttle closed
  Ignition off, Master off when RT complete
  Fuel off
  Security – check harness tight, reassure passenger

## Slide 27
1
Fly The Aircraft
2
Estimate Wind
3
Select Landing Area
4
Fly the Plan
Wind
Approx 1000’ AGL
Constant angle
Constant Aspect Method
High Key Point
(min sink and trim)
1400 AGL
Best Glide
Flaps as required
Approx 300’ AGL
Low Key Point
Wings level
Flaps as required
INITIAL AIM 1/2
FINAL AIM 1/3
IF TOO LOW
IF TOO HIGH
Sideslip / S-turns
Mayday Call
5
Attempt Restart
6
T.I.F.S Check
7
Approx 500’ AGL

## Slide 28
1
Fly The Aircraft
2
Estimate Wind
3
Select Landing Area
4
Fly the Plan
Wind
Approx 1000’ AGL
Constant angle
Constant Aspect Method
High Key Point
(min sink and trim)
100 AGL
Best Glide
Flaps as required
Approx 300’ AGL
Low Key Point
Wings level
Flaps as required
INITIAL AIM 1/2
FINAL AIM 1/3
IF TOO LOW
IF TOO HIGH
Sideslip / S-turns
Mayday Call
5
Attempt Restart
6
T.I.F.S Check
7
Approx 500’ AGL

## Slide 29
Keep in balance during turns and monitor safe A/S
Try to limit turns to 30 deg bank angle
Flaps as appropriate
1200 AGL
Beats and Turns Method
If too low for circuit method
INITIAL AIM 1/2
Full Flaps /Sideslip
Wings level
FINAL AIM 1/3
Wind
Best Glide
1st Stage flaps
Position aircraft on Beat line/Base leg
1
Fly The Aircraft
2
3
Asses Wind
Select Landing Area
Fly the Plan
4
REFERENCE LINE OR POINT
To prevent aircraft migration towards field
Mayday Call
5
Attempt Restart
6
T.I.F.S Check
7

## Slide 30: Landing
Touchdown
  Surface unknown, so land as softly as possible and fully held off to minimise touchdown speed
  If landing on crop treat top of crop as landing surface
After landing
  Secure aircraft – check position and livestock
  Cancel mayday – by radio or phone
  Notify destination within 30 mins of your planned arrival time
  Notify land owner
  Consider very carefully take off and only if absolutely sure cause identified and rectified

## Slide 31: Airmanship for Practice Engine Failure
Lookout
Be mindful of the 500’ rule
Choose multiple sites to practice – don’t be a nuisance
Consider the descent and climb out path
  Always be ready for real engine failure
  Ensure decent and climb out are free from obstructions
Warm engine in the descent
  Helps prevent carburettor icing
  When going around increase power gradually and raise nose, then retract flaps in stages
Manage airspeed in go around – respect Vfe

## Slide 32: Exercise 16a Forced Landings
Questions?

## Slide 33
(min sink 45 Kts and trim)
Approx 500’ AGL
Approx 1000’ AGL
Constant angle
IF TOO HIGH
Sideslip / S-turns
INITIAL AIM 1/2
FINAL AIM 1/3
Best Glide
Flaps as required
(best glide 58Kts and trim)
Attempt Restart
T.I.F.S Check
Mayday Call
1
2
3
4
Fly The Aircraft
2000 AGL
Asses Wind
Select Landing Area
Fly the Plan
Constant Aspect Method
Approx 300’ AGL
IF TOO LOW
High Key Point
Low Key Point
5
6
7
Wings level

## Slide 34
1
Fly The Aircraft
Keep in balance during turns and monitor safe A/S
Try to limit turns to 30 deg bank angle
Flaps as appropriate
Full Flaps /Sideslip
INITIAL AIM 1/2
Wings level
2
3
1000 AGL
Asses Wind
Select Landing Area
Fly the Plan
REFERENCE LINE OR POINT
To prevent aircraft migration towards field
4
Beats and Turns Method
Position aircraft on base leg
If too low for circuit method
FINAL AIM 1/3
Best Glide
1st Stage flaps