## Slide 1: Exercise 7 Basic Climbing and Descending
Aim - as syllabus
Phase 2
Copyright Marcus Furniss 2019

## Slide 2: Theory – Forces in Level Flight
LIFT = WEIGHT
THRUST
DRAG
LIFT
WEIGHT
THRUST = DRAG

## Slide 3: Theory – Forces in a Climb
Therefore more THRUST required
A component of WEIGHT acts with DRAG
THRUST
LIFT
WEIGHT
DRAG
This component of weight acts with DRAG
This component of weight opposes LIFT

## Slide 4: Theory – Forces in a Glide Descent
WEIGHT
A component of weight acts as THRUST
LIFT
DRAG
This component of weight adds to THRUST
This component of weight opposes LIFT

## Slide 5: Climb Entry
P
Power – Increase power and balance with rudder
Attitude – Raise nose to climbing attitude and hold
Trim – Adjust attitude to achieve correct airspeed, hold and trim
EV-97 90 MPH
C42 80 KTS
EV-97 80 MPH
C42 70KTS
Reference Point – due high nose attitude use VRP to left to maintain straight flight
A
T

## Slide 6: To Level Off
Anticipate – initiate the levelling-off procedure at 20 feet before the target altitude
Attitude – Lower nose to level attitude and hold until target airspeed achieved
Power – reduce to cruise RPM and balance with rudder
Adjust attitude to achieve correct airspeed, adjust power to maintain height then hold and trim
EV-97 90 MPH
C42 80KTS
Trim –
EV-97 80 MPH
C42 70KTS
A
P
T
20 feet

## Slide 7: Descent Entry Target descending airspeed is lower than cruise airspeed
EV-97 80 MPH
C42 70KTS
Adjust attitude /power to achieve correct airspeed and descent rate, then hold and trim
Power Reduce as required and keep in balance with rudder
Attitude
Hold initially as airspeed reduces to target airspeed and then lower to descent attitude
Trim
EV-97 90 MPH
C42 80 KTS
P
A
T

## Slide 8: Descent Entry Target descending airspeed is same or greater than cruise airspeed Also default technique for older microlight types
EV-97 90 MPH
C42 80 KTS
Adjust attitude /power to achieve correct airspeed and descent rate, then hold and trim
Attitude Lower nose to descent attitude and hold
Power
Reduce as required, use rudder to keep balance
Trim
EV-97 90 MPH
C42 80 KTS
A
P
T

## Slide 9: To Level Out from a Descent
Power – Increase power and balance with rudder
Attitude – Raise nose to level attitude and hold
Anticipate – initiate the levelling-off procedure at 50 feet before the target altitude
+
P
A
Trim – Adjust attitude to achieve correct airspeed and trim
T
EV-97 90 MPH
C42 80 KTS
EV-97 80 MPH
C42 70KTS
50 feet

## Slide 10: To enter a Climb from a Descent
Power – Increase power and balance with rudder
Attitude – Raise nose to climbing attitude and hold
+
P
A
Trim – Adjust attitude to achieve correct airspeed then hold and trim
T
EV-97 80 MPH
C42 70KTS
EV-97 80 MPH
C42 70KTS

## Slide 11
EV-97 80 MPH
C42 70KTS
Adjust attitude /power to achieve correct airspeed and descent rate, then hold and trim
Attitude Lower nose to descent attitude and hold
Power
Reduce as required, use rudder to keep balance
Trim
EV-97 80 MPH
C42 70KTS
A
P
T
To enter a Descent from a Climb
  If flaps are extended nose attitude will need to be lower to maintain airspeed
  In transition period aircraft may be significantly out of trim

## Slide 12: Cruise climb and descent
Cruise Climb
Less than full power will reduce angle and rate of climb
Less stress on engine and lower noise
Lower nose attitude for same airspeed
Cruise descent
Adding power will reduce angle and rate of descent
Used to control descent rate (ie when approaching to land)
Keeps engine warm during prolonged descent

## Slide 13: Airmanship
Lookout – all around and above before and during climb, all around and below before and during descend
Blindspots – lower nose every 500 feet in climb, check below with pax lookout before descent
Airspace - what type above and below and can we comply?
Altimeter – correct pressure set, usually the Manchester QNH
Cloud – ensure we remain clear as appropriate for airspace and altitude
Engine – monitor T’s and P’s

## Slide 14: Exercise 7 Basic Climbing and Descending
Questions?

## Slide 15: Exercise 8 Performance Climbing and Descending
Aim - as syllabus
Phase 2

## Slide 16: Theory – Climb Performance
Published performance of our aircraft is valid for International Standard Atmosphere (ISA)
Temperature +15 Degrees Celsius
Pressure 1013 hPa
Air density 1225 grammes per cubic metre
Altitude at sea level
Climb performance will degrade with
Increased altitude
Increased humidity
Increased temperature
Low atmospheric pressure
Increased weight
Flaps setting will effect climb performance
Airspeed will effect climb performance

## Slide 17: Theory – Effect of Airspeed on Climb Performance
Drag varies with airspeed, so climb performance will also vary with airspeed
Vy (Best Rate)
70 mph EV-97
60 KTS C42
Typical safe climb
80 mph EV-97
70 KTS C42
Vx (Best Angle)
62 mph EV-97
48 KTS C42
Typically 700 feet per minute
Typically 1000 feet per minute
Typically 900 feet per minute

## Slide 18: Theory – Effect of Airspeed on Glide Performance
Typically 500 feet per minute
In a glide different airspeeds will give different descent performance
Best Glide
68 mph EV-97
58 KTS C42
Typical descent
80 mph EV-97
70 KTS C42
Min Sink
60 mph EV-97
45 KTS C42
Typically 1000 feet per minute
Typically 400 feet per minute

## Slide 19: Theory – Effect of Flaps on Climb Performance
Consult aircraft POH as effects vary with type
  Small deflection may improve climb angle (ie C42), but not rate
  Large deflection will degrade climb performance markedly
  Lower pitch attitude is required to maintain airspeed
Flaps create same lift at lower speed
  Stall speed reduces
  Allows safer flight at slower airspeed
Use small deflection for take off
  Allows lower rotation speed and shorter take off distance

## Slide 20: Theory – Effect of Flaps on Descent Performance
Drag flaps (large deflections) are often used for approach and landing
  Lower pitch attitude required to maintain airspeed (this also affords better visibility ahead)
  Higher rate and angle of descent in glide
Flaps create same lift at lower speed therefore stall speed reduces
  Allows safer flight at slower airspeed
Use large deflection for landing
  Allows reduction in landing speed and landing distance

## Slide 21: Theory – Effect of Flaps on Descent Performance
1st Stage - 60mph
2nd Stage - 60mph
3rd Stage - 60mph
No flaps - 60mph

## Slide 22: Go Around – WHY?
Power – Increase power and balance with rudder
+
P
A
Trim – Adjust attitude to achieve correct airspeed and trim
T
EV-97 60 MPH
C42 55 KTS
EV-97 60 MPH
C42 55 KTS
Attitude – Raise nose to shallow climb attitude and hold
  If flaps are extended nose attitude will need to be lower to maintain airspeed
  Once positive rate of climb is established retract flaps in stages, managing airspeed with pitch
  In transition period aircraft may be significantly out of trim

## Slide 23
EV-97 70 MPH
C42 55 KTS
Adjust attitude /power to achieve correct airspeed and descent rate, and trim
Attitude Lower nose to descent attitude and hold. If flaps are extended nose attitude will need to be lower to maintain airspeed
Power
Reduce as required, use rudder to keep balance. If large power change, significant adjustment s to rudder and aileron may be required
Trim
EV-97 70 MPH
C42 55 KTS
A
P
T
To enter a Descent from a Climb
  In transition period aircraft may be significantly out of trim

## Slide 24: Side Slipping
A slide slip is where
  Rudder and aileron are applied simultaneously in opposite directions (cross controlling)
  Aircraft flies sideways in relation to airflow creating more drag
  Pro spin configuration so control airspeed accurately using attitude
Side slipping is a technique used in a glide descent to increase decent rate without increasing airspeed

## Slide 25: Airmanship
Lookout – all around and above before and during climb, all around and below before and during descend
Blindspots – lower nose every 500 feet in climb, check below with pax lookout before descent
Airspace - what type above and below and can we comply?
Altimeter – correct pressure set, usually the Manchester QNH
Cloud – ensure we remain clear as appropriate for airspace and altitude
Engine – monitor T’s and P’s

## Slide 26: Exercise 8 Performance Climbing and Descending
Questions?